## Slide 1: Combustion Regime-Independent Sub-grid Turbulent Combustion Model for Accurate Numerical Simulations of High-speed Turbulent Reacting Flows
Fernando Illacanchi1,3,*, Andrés Z. Mendiburu2, Cesar Celis1
1Mechanical Engineering Section, Pontificia Universidad Católica del Perú, Lima, Peru
2Universidade Federal do Rio Grande do Sul, Porto Alegre, Brazil
3Technical University of Munich, TUM School of Engineering and Design, Garching, Germany
*f.illacanchi@pucp.edu.pe

## Slide 2
Motivation
High-speed reacting flows include shockwaves, autoignition, and turbulent flame front: one model must hold across regimes
In LES, the filtered source requires a closure.
PSR ignores turbulence-chemistry interaction.
Transported PDF is regime-independent, but molecular mixing is still modeled
Linear-eddy model (LEM) resolves turbulent advection, diffusion, and reaction on a 1D line.
High-speed flame propagation in an obstructed channel

## Slide 3
Governing equations
LES: mass, momentum, and energy
Resolved: , with
Chemical reaction source:
P-CLEM: two-scale split
Over one step:
: particle advection across faces (splicing)
: cell interior
LES
P-CLEM
subordinate
to LES
energy-consistent
Flowchart for LES – CLEM numerical simulation

## Slide 4
LEM Representation
Each LEM domain is an ordered particle ensemble carrying T, Y, mass, volume, and pressure.
Mass coordinate: thermal expansion is intrinsic
Built on AMReX particles in PeleC, allowing scalability.
Computational representation of the particle ensembles in a LES cell. Particle ensembles are oriented in the flow direction.

## Slide 5
Stirring and resolved field effect
A priori assessment:
  The eddy size that carries most of the molecular mixing (stirring) is only cell size dependent , with (, not influenced by flow state.
  Frequency of the stirring effect is heavily determined by the turbulence closure
  Effect: particles are reordered, high-order statistics are held, and gradients steepen so molecular mixing acts faster
Before stirring: particles ordered 1–16
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
1
2
3
4
5
8
11
12
9
6
7
10
13
14
15
16
After stirring
Stirring effect on a particle ensemble. Stirring is a permutation of particles enhancing scalar gradients.

## Slide 6
Particle advection - Splicing
Three-dimensional mechanism represented by a one-dimensional domain.
Total scalar is conserved by the particle method
Diffusion is orthogonal to the mean flow direction.
Notable effect of the number of particles.
Advection of a square-shaped scalar field
Scalar field along the main flow direction (left) and orthogonal direction (right) for different numbers of particles.

## Slide 7
Premixed flame - PMF
Lean premixed flame, φ = 0.4, 300 K, 1 atm: 128 cells × 12 particles against a 512-cell reference
The energy-consistent coupling strategy is validated.
A small shift in the mass species curve is due to the splicing operator.
Chemical heat release is accounted for in the particle internal energy.
CLEM coupling update (mass-weighted)
φ̃n+1 = φ̃* + ΔφCLEM
ΔφCLEM = Σp mp (φpn+1 − φpn) / Σp mp
φ̃* = φ̃n for Yk (not solved by NS)
φ̃* = NS solution for energy
Schematic of the flow configuration
OH mass species (left) and temperature (right) profiles

## Slide 8
Non-reacting Cross-jet flow
Sonic H2 jet (Dj = 1 mm) into a Mach 1.5 air crossflow at 1000 K, 1 atm (Case 1, Jin et al.)
400 × 48 × 16 cells, 0.3125 mm, no AMR
Hairpin vortices persist to x = 10 cm with WALE-WM, only to x = 8 cm with Smagorinsky.
Q-criterion using WALE (top) and classical Smagorinsky (bottom) model

## Slide 9
Effect of turbulence closure
Stirring rate set by the LES eddy viscosity:
Stirring events: ≈ 900 with WALE-WM vs ≈ 6 × 104 with Smagorinsky
Subgrid mixing inherits the turbulence-closure error.
Number of stirring events per time step using different turbulence closure

## Slide 10
Conclusions
P-CLEM is implemented in PeleC with a mass-conserving, energy-consistent coupling.
0D reactor and premixed flame reproduce the references within 0.1 K
Splicing and regridding conserve scalars globally, but add local spurious diffusion.
Subgrid mixing frequency is set by the LES eddy viscosity (Λ ∝ νt17/12): ≈ 6 × 104 vs ≈ 900. The closure is critical to accurately predict turbulent flames.
Combustion and turbulence closures cannot be assessed independently.
This work is the baseline framework for further development, including AMR in the particle domain to simulate complex flow configurations accurately.
The authors acknowledge the support of the National Council for Science, Technology and Technological Innovation (CONCYTEC, Peru) through the PROCIENCIA program, under the 2025-01 Basic Research Projects call (Contract No. PE501095038-2025-PROCIENCIA)